## Slide 1
Electrical Wire Types for Electrical Systems
Name : Ayush Kumar Prajapati
Department : Computer Science and Engineering
Section: PU
Roll no: 4
IEE AAT

## Slide 2
Electrical Wire Types for Electrical Systems
This presentation explores common electrical wire types, their properties, and application.
Vulcanized Indian Rubber (V.I.R.) Wires
Construction & Features
Rubber insulation
Tinned conductor
Cotton braiding
Wax coating
Applications
Low/medium voltage
Older installations

## Slide 3
Tough Rubber Sheathed (T.R.S.) Wires
Construction & Features
V.I.R. with tough rubber sheath
Moisture, wear, and damage resistance
Single, twin, and three-core versions
Applications
Industrial and commercial installations
Temporary outdoor wiring

## Slide 4
Poly Vinyl Chloride (P.V.C.) Wires
Most Common
PVC thermoplastic insulation
Moisture, chemical, and wear resistance
Widely Used
Household wiring
Industrial electrical systems
Indoor and outdoor applications

## Slide 5
Lead Alloy Sheathed Wires
Construction & Features
Outer lead sheath for protection
Moisture-prone environments
0.12 cm thick sheath
Applications
Underground installations
Industries and damp environments

## Slide 6
Weatherproof Wires
Construction & Features
Fibrous yarn saturated with waterproof compound
Rain, humidity, and UV radiation resistance
Applications
Service connections from power lines to buildings
Agricultural applications and outdoor lighting

## Slide 7
Flexible Wires
Construction & Features
Multiple fine strands
PVC insulation
Frequent movement applications
Applications
Household appliances
Automotive wiring
Portable electrical devices

## Slide 8
Choosing the Right Wire
1
Insulation Material
Determines resistance to moisture, heat, and chemicals
2
Mechanical Strength
Impact resistance, flexibility, and durability
3
Environmental Conditions
Exposure to moisture, temperature, and UV radiation